## Slide 2: Chapter 5 Network Commands
Network and Security Fundamentals

## Slide 3: Objectives
Explain the use of a graphical user interface (GUI) and command line interface (CLI)
Describe Transmission Control Protocol/Internet Protocol (TCP/IP) commands including ping, ipconfig, and tracert
Identify the best command to use in a troubleshooting scenario
Describe network troubleshooting methods and approaches

## Slide 4: Chapter 5- GUI and CLI
GUI- Graphical User Interface
CLI- Command Line Interface

## Slide 5: Chapter 5 CLI Access
Telnet -Telnet is a network protocol that permits a user to connect with a remote device. Telnet data is sent in clear text. Telnet establishes a connection by using the TCP port 23 by default. Common Telnet servers are Putty, 3cdaemon, and TeraTerm.
Secure Shell (SSH) - SSH is a network protocol that permits a user to connect with a remote device. SSH uses public key cryptography to make sure all transmissions are secure.

## Slide 6: Chapter 5- TCP/IP Commands
The most common tools used in the troubleshooting process are ping, ipconfig, and tracert.
Traceroute uses Internet Control Message Protocol (ICMP) echo packets to display information of each hop that it travels through.
Ping is often used to check connectivity between two nodes on the network.
The ipconfig command can be used to view information such as the host’s IP address, the subnet mask, the interface name, and the default gateway.

## Slide 7: Chapter 5- Network Errors
Request timed out
Destination Host Unreachable
Bottleneck
Unknow Host

## Slide 8: Chapter 5- (TTL) Time to live
The Time to live (TTL) value is extremely important in comprehending the ping command. The purpose of the TTL is to prevent a packet from being on the network for an extended amount of time and to prevent circular routing. Circular routing arises when a ping request continues to loop through a series of network host. A simpler way to think of a TTL is the number of hops or time a packet exists in a network prior to being discarded.

## Slide 9: Chapter 5- Network Troubleshooting
Network Troubleshooting - A specific network issue or problem can be analyzed and resolved several different ways. However, all troubleshooting should be done with a methodical approach. Using a systematic and well-thought-out approach allows for continues progress.
By methodically removing potential problem causes, a user can minimize the scope of issues until they are able to isolate and resolve the problem.

## Slide 10: Chapter 5- Troubleshooting Methods
Top-down approach
Bottom-up approach
Divide-and-conquer